CoAP an introduction
Bifrost workshop
2012-11-28
Robert Olsson KTH/UU

---
CoAP/overview
- Internet-Of-Things (IoT)
- CoAP (Constraint Application Protocol)
- IETF standard (Draft)

---
CoAP/overview
- Machine-to-Machine (M2M)
- Small footprint, RAM, ROM
- URI (Uniform Resource Identifier)
  mapping considered

---
CoAP/overview
- RESTful client server compare http:
- Resource Discovery
- UDP
  - Reliable unicast
  - Best effort multicast
- Proxy and Caching is simple

---
CoAP/message type
- Comfirmable message
- Non-comfirmable message
- Ack message
- Reset message
  - Piggy-backed
  - Seprate

---
CoAP/transport
- Default UDP but required
  DTLS (Datagram TLS)
- TCP
- SCTP

---
CoAP/protocol
- 4 byte header
- Options
- Payload
  - uint (unsigned integer)
  - string
  - opague
- Endpoint
  - IP addr, UDP port

---
CoAP/protocol header
  0 1 2 3
    0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   |Ver| T | OC | Code | Message ID |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | Options (if any) ...
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | Payload (if any) ...
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
        Figure 7: Message Format
3.1. Header Format
   The fields in the header are defined as follows:
   Version (Ver): 2-bit unsigned integer. Indicates the CoAP version
      number. Implementations of this specification MUST set this field
      to 1. Other values are reserved for future versions.
   Type (T): 2-bit unsigned integer. Indicates if this message is of
      type Confirmable (0), Non-Confirmable (1), Acknowledgement (2) or
      Reset (3). See Section 4 for the semantics of these message
      types.
   Option Count (OC): 4-bit unsigned integer. Indicates the number of
      options after the header (0-14). If set to 0, there are no
      options and the payload (if any) immediately follows the header.
      If set to 15, then an end-of-options marker is used to indicate
      the end of options and the start of the payload. The format of
      options is defined below.

---
CoAP/pkt-size
- Message size
  - Must fit in a single IP datagram
    - Default MTU 1280 bytes
    - 6LOWPAN 127 bytes
    - WSN based on IEEE 802.15.4 127 bytes

---
CoAP/RESTful
- CoAP Request/Response semantics
  - GET, POST, PUT, DELETE
    Easy to map to HTTP
- Cache and Proxy possible
- Token to match. Request/Respose pairs

---
CoAP/URI
coap URI
  coap://example.se:5683/~sensors./temp1.xml
coaps URI
  coaps://example.se:XXXX/~sensors./temp1.xml

---
CoAP/Resouce Discovery
Endpoint resource discovery (IP addr is known)
  (Knowing or learning URI namspace)
  - ct (content type) web linking RFC5988
  - Multicast: ALL-COAP-NODES
    - Some tricks to read.

---
CoAP/Secure
  - DTLS (Datagram TLS)
  - IPSEC alternative
    - Key sharing problems
    - Resource problems
    - Cerificate problems

---
CoAP/HTTP mapping
  - Request/Response model is mapped HTTP
    - Not messages, non-confirmable
  - Proxy CoAP → HTTP
  - Proxy HTTP → CoAP
  - Proxy is man-in-the middle
    - Security issues
    - Key sharing problems
    Caching. Consider.

---
CoAP/implementations
  - Contiki-2.6
    - ETH Zurich
      - 8.5 kB ROM
      - 1.5 kB RAM
  - Linux → libcoap
  - TinyOs (libcoap)
  - Firefox CoAP plugin

---
CoAP/example
Client Server
      | |
      | |
      +----->| Header: GET (T=CON, Code=1, MID=0x7d34)
      | GET | Uri-Path: "temperature"
      | |
      | |
      |<-----+ Header: 2.05 Content (T=ACK, Code=69, MID=0x7d34)
      | 2.05 | Payload: "22.3 C"
      | |
    0 1 2 3
    0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | 1 | 0 | 1 | GET=1 | MID=0x7d34 |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | 11 | 11 | "temperature" (11 B) ...
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
    0 1 2 3
    0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | 1 | 2 | 0 | 2.05=69 | MID=0x7d34 |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | "22.3 C" (6 B) ...
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
        Figure 16: Confirmable request; piggy-backed response

---
CoAP/additional standards
- Blockwise transfers in CoAP (16-1024 bytes)
  draft-ietf-core-block-10
- CoRE Link Format (GET /.well known/core)
  draft-shelby-core-link-format-14
- Observing Resources in CoAP (Observe option)
  draft-ietf-core-observe-07

---
References
The Contiki OS. http://www.contiki-os.org/
draft-ietf-core-coap-12 https://datatracker.ietf.org/doc/draft-ietf-core-coap/
draft-ietf-core-block-10 https://datatracker.ietf.org/doc/draft-ietf-core-block/
draft-ietf-core-observe-07 https://datatracker.ietf.org/doc/draft-ietf-core-observe/
draft-ietf-core-link-format-14 https://datatracker.ietf.org/doc/draft-ietf-core-link-format/
M. Kovatsch, S. Duquennoy, and A. Dunkels, A Low-Power CoAP for
Contikiâ in Mobile Adhoc and Sensor Systems (MASS), 2011 IEEE 8th International Conference on, 2011, pp. 855-860, DOI:10.1109/MASS.2011.100.
IANA: RFCUniform Resource Identifier (URI) Schemes. [RFC4395]
R. Olsson and J. Laas, Sensd. http://github.com/herjulf/sensd.

---
Questions

---
- CoAP/HTTP
- Questions