Refeshing basics in
Networking, IP and routing
Robert Olsson KTH/CSD

---
Most slides from:
KTH Computer Science Course
Thanks to: Olof Hagsand KTH/CSC
[Speaker Notes: Welcome to DD2392/EP2120]

---
The Hourglass Model
- Anything over IP – IP over anything
- All applications depend on IP
- IP runs over all networks
- IP is at the heart of all communication
 email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP
  ethernet PPP…
CSMA async sonet...
 copper fiber radio...
From Steve Deering, 2000

---
Layering: The TCP/IP stack
The TCP/IP stack and OSI ref model
L7: Application
DNS
...
SMTP
HTTP
FTP
SSH
L6: Presentation
L5: Session
UDP
SCTP
TCP
L4: Transport
L3: Network
IP
ARP
L2: Data Link
WLAN
...
Ethernet
PPP
ATM
L1: Physical
ICMP IGMP

---
Layering in TCP/IP
Host/
End system
Host/
End system
Router
TCP
TCP
  IP
       IP
  IP
LINK
LINK
MAC
LINK
PHY
PHY
PHY
PHY
LAN
LAN

---
Layering example
Network
Data Link
Physical
Fredrik Gunger

---
Encapsulation – decapsulation
Encapsulation
Include data from
higher layer protocols into lower layer protocols
using headers
Appl
header
L7
TCP
header
L4
Segment
IP
header
L3
Datagram
Ethernet
header
Ethernet
trailer
Payload
L2
Frame
4
14
20
20
User data
Ethernet frame
46 to 1500 bytes
Payload
        Payload
        Payload

---
Multiplexing – de-multiplexing
Multiplexing and Demultiplexing
...
...
Processes
Port number in
transport header
Protocol type in
IP header
ARP
Payload type in
Ethernet header
Multiple higher layer protocols are mixed into the same lower layer protocol
Packet
Application
TCP
UDP
IP
ICMP
IGMP
Ethernet
Application
Application
Application

---
The End2End Argument
A specific application-level function should not be built into the lower levels of the system.
- The functions “in” the Internet are simple and general.
- The bulk of functions are in software at the “edge”.
- The complexity of the core network is reduced.
- Generality in the network increases the chances that new applications can be added.
Saltzer, Reed, Clark, 1984, Blomenthal & Clark 2001

---
Standards: Organizations
- Internet standard groups
  - ISOC – Internet Society
    - IAB – Internet Architecture Board
    - IETF – Internet Engineering Task Force
  - IANA – Internet Assigned Numbers Authority
    - ICANN – Internet Corporation for Assigned Names and Numbers
- Related
  - ISO – International Standards Organisation
  - IEEE – Institute of Electrical and Electronics Engineers
  - ITU-T – International Telecommunications Union – Telekom sector
  - W3C – World-Wide-Web Consortium
  - ...

---
IEEE 802 vs IPv4 addresses
vendor code
vendor assigned
IEEE
802
10111101
10111101
10111101
10111101
10111101
10111101
10111101
01110101
10111101
01110101
10111101
01110101
Group/
Individual bit
00:0E:35:64:E9:E7
Global/
Localbit
netid
hostid
10111101
10111101
10111101
10111101
11000000
00100100
01111101
00010010
IPv4 addr
192.36.125.18

---
IP-numbers (private)
3. Private Address Space. (RFC1918)
The Internet Assigned Numbers Authority (IANA) has	reserved:
     10.0.0.0 - 10.255.255.255 (10/8 prefix)
     172.16.0.0 - 172.31.255.255 (172.16/12 prefix)
     192.168.0.0 - 192.168.255.255 (192.168/16 prefix)
Used for NAT and experiments

---
Levels of abstraction
Internal vs external routing
- The Internet is huge
  - Necessary to divide the routing problem into sub-problems.
  - The “Internet” is divided into Autonomous systems (ASs)
  - Each AS is independently managed
- Inter-domain routing / External routing
  - Routing between AS:s
  - Based on commercial agreements – Policies, Service-level-agreements
- Intra-domain routing / Internal routing
  - Routing inside an AS
  - An AS may be further divided into areas
  - Best path based on hop metric
- Static vs Dynamic routing

---
IGP/EGP
IGP/EGP
ISP
Customer
EGP
IGP
IGP
EGP
  - Exterior Gateway Protocol.
  - Runs between networks/domains (inter-domain)
  - Examples: BGP, static routing
IGP
  - Interior Gateway Protocol.
  - Runs within a network/domain (intra-domain)
  - Examples: RIP, OSPF, IS-IS.

---
Popular Unicast Routing Protocols
Routing Protocols
Interior
Exterior
BGP
RIP
OSPF
IS-IS
IGRP
(cisco)
EGP

---
IP topology example

---
Routers: Cisco CRS-1
CISCO's current flagship:
Carrier- Routing System
3-stage multi-stage switching plane
>50% of cost
Trie prefix lookup
7.5kW
Each slot has 40Gbps
32Tbps raw bandwidth
Distributed RP
Several Logical Routers
Optical_Electric transitions:
O-E-O-E-O-E-O

---
Juniper Routers
Routers: Juniper
- M-series
  - Shipping started 1998
  - M5, M10, M20, M40e, M160, M320
  - 8xOC-192 or 32xOC-48
    ports in a M160
- T-series
  - Shipping started 2002
  - T320, T640
  - 32xOC-192 or 128xOC-48
    ports in a T640
Capacity: 80Gb/s
Power: 2.6kW
19”
3ft
2.5ft
Juniper M160

---
Routers: Linux based
- Linux, BSD platforms
- Most routing protocols exist as open source projects
- But PC HW has traditionally been a limiting factor
- Now quad core CPUs, new buses (PCI express), 10Gbps NICs enables gigabit forwarding speeds.
- Example: the Bifrost from
  (UU/KTH)
- Linux is used in most AP
  and firewalls

---
Linear Search on Length Using a Trie
Linear Search on Length Using a Trie
- Binary tree
  - Nodes are prefixes
  - Left branch represents ´0´in the string
  - Right branch represents ´1´
a *
b 10*
c 01*
d 110*
*
a
e 0010
f 0110
g 0111
0*
1*
10*
b
00*
01*
11*
c
d
000*
011*
110*
0010
e
f
g
0110
0111

---
LC-trie routing lookup
- Routings algorithms a high researched area
- LC trie contribution by Stefan Nilsson, Gunnar Karlsson @ KTH
- Further refined and first implemented and for Linux kernel
  Robert Olsson, Hans Liss, Jens låås, Uppsala University and Swedish
  university of agricultural sciences. About 3 man-years and lots of support
  for Linux Networking Team
- Got Intel Academic Award 2005
*

---
What is BGP?
- Border Gateway Protocol version 4
- Defined in RFC 4271
- An inter-domain routing protocol
- Uses the destination-based forwarding paradigm
  - No other relations can be expressed: sources, tos, link load
- Uses path-vector routing
- Views the Internet as a collection autonomous systems
- Exchanges information between peers using TCP as underlying protocol
- Maintains a database (RIBs) of network layer reachability information (NLRI:s)
- Supports a toolkit of mechanisms to express and enforce policies decisions at the AS level

---
The routing table
- Currently, backbone IP tables are around 300000 entries.
  - The RIB may be much larger
- Virtual private networks (many customer routing tables) the tables are even larger
- Also, a “routing table” is actually many data-structures:
  - Many different protocols
  - Forwarding information base (FIBs)
  - Routing information base (RIBs)

---
Autonomous Systems
Autonomous Systems (AS)
- A set of routers that has a single routing policy, that run under a single technical administration
  - A single network or group of networks
  - University, business, organization, operator
- This is viewed by the outside world as an Autonomous System
  - All interior policies, protocols, etc are hidden within the AS
- Represented in the Internet by an Autonomous System Number (ASN). 0-65535
  - Example: ASN 1653 for SUNET
  - Note: RFC 4893: BGP Support for Four-octet AS Number Space

---
Stub AS
Customer / ISP Relations:
Stub AS
Provider
Announced networks, traffic flows in other direction
Customer
- Typical customer topology
- Can use default route to reach the Provider and Internet
- Customer can use address block of provider
- Customer does not need to be a separate AS
- Typically use static routing but can also use BGP
  - Less common. Use a separate IGP (eg RIP) only to exchange routes between border routers.
n1, n2
default
n1, n2

---
AS graph and peering relations
Tier 1: Full
Internet
connectivity
AS1
AS2
Transit
AS5
AS3
AS4
Peer
NSPs
ISPs
Customer
AS6
AS7
AS8
AS9
Stubs/
Customers
[Speaker Notes: Based on information exchanged between BGP routers, a graph of Autonomous systems can be constructed. This is sometimes refered to as a tree. Why is it important to construct a graph? You have to understand that the real world, there are thousands of ASes interconnected. It is impossible for everyone to connect to everyone. So, with this in mind, BGP was design to be used between two adjacent AS to exchange path information, Which eventually used to construct the network topology. Connections between 2 AS form a path while a collection of path information forms a route to reach a specific destination. BGP uses the path information to ensure loop-free interdomain routing. That’s the overview of BGP, now let’s see how BGP works?]

---
Cost and peering relations
You pay for transit traffic.
You pay for transit traffic.
Full
Internet
connectivity
AS1
AS2
Transit
-$
-$
AS5
AS3
AS4
Peer
NSPs
ISPs
0
Customer
+$
+$
AS6
AS7
AS8
AS9
Stubs/
Customers
[Speaker Notes: Based on information exchanged between BGP routers, a graph of Autonomous systems can be constructed. This is sometimes refered to as a tree. Why is it important to construct a graph? You have to understand that the real world, there are thousands of ASes interconnected. It is impossible for everyone to connect to everyone. So, with this in mind, BGP was design to be used between two adjacent AS to exchange path information, Which eventually used to construct the network topology. Connections between 2 AS form a path while a collection of path information forms a route to reach a specific destination. BGP uses the path information to ensure loop-free interdomain routing. That’s the overview of BGP, now let’s see how BGP works?]

---
Traffic patterns
Note where there are no traffic arrows!
Full
Internet
connectivity
AS1
AS2
Transit
AS5
AS3
AS4
Peer
NSPs
ISPs
Customer
AS6
AS7
AS8
AS9
Stubs/
Customers
[Speaker Notes: Based on information exchanged between BGP routers, a graph of Autonomous systems can be constructed. This is sometimes refered to as a tree. Why is it important to construct a graph? You have to understand that the real world, there are thousands of ASes interconnected. It is impossible for everyone to connect to everyone. So, with this in mind, BGP was design to be used between two adjacent AS to exchange path information, Which eventually used to construct the network topology. Connections between 2 AS form a path while a collection of path information forms a route to reach a specific destination. BGP uses the path information to ensure loop-free interdomain routing. That’s the overview of BGP, now let’s see how BGP works?]

---
IP resources
- IP numbers Ipv4 (exhausted when?)
- IP numbers IPv6
- AS-numbers 16 vs 32 bit
- PI Provider Independent
  PA Prover Aggregable
  - LIR, AfriNIC or through provider.

---
What drives deployment?
IPv6: What drives deployment?
- Asia and Europe
  - Smaller pools of IPv4 addresses
  - Faster at adopting new technology
  - Government-driven (ASIA)
  - Wireless (3G in Europe)
- U.S.
  - DoD announced that it will move to IPv6 by 2008
    - Public address assignment simplifies end-to-end security
- IPv6 has been added to DNS root servers
- SUNET and NorduNET runs IPv6 in core

---
IPv6 vs IPv4
IPv6 vs IPv4
- Changes in IPv6 compared to IPv4
  - 128 bit addresses
  - extended address hierarchy
  - simplified header
  - simpler and better support for options
  - possible to extend the protocol
  - support for auto-configuration (plug-and-play)
  - support for QoS treatment
  - host mobility
  - security
  - provider selection
  - no fragmentation in routers

---
IPv6 Header Format
IPv6 Header Format
0
15
16
31
4-bit
Version
8-bit
Class
20-bit Flow Label
8-bit
Next Header
8-bit
Hop Limit
16-bit Payload Length
128-bit Source Address
128-bit Destination Address
- Version	Only field identical to IPv4. Code is 6 in IPv6
- Class	New field. Revised concept of priority bits. Facilitates handling of real-time traffic.
- Flow Label	New field. To distinguish packets requiring the same treatment.
- Payload LengthReplaces length field in IPv4. Gives length of data following IPv6 header
- Next Header	Replaces protocol field in IPv4. Extension headers can be used.
- Hop Limit	Replaces TTL field in IPv4. Hop limit more accurately reflects the use of TTL.
- Src Address	Revised source address field. 128 bits in IPv6 vs 32 bits in IPv4.
- Dst Address	Revised destination address field. 128 bits in IPv6 vs 32 bits in IPv4.
40 bytes

---
What wasn't mentioned
- Different services /etc/services
- ICMP Internet Control Messages Protocol
- ARP
- UDP nor TCP
- NAT
- DNS
- Ipsec, SSL
- Filtering

---
That's all
Questions?